Technical Objectives:

- Calculate the adiabatic flame temperature and final equilibrium product mole fractions using the conservation of energy, along with the kp equilibrium constants.

- Calculate the actual chemical composition of combustion products assuming equilibrium conditions at a prescribed final pressure and temperature using NASA CEA.

- Calculate the adiabatic flame temperature for a given set of reactants using NASA CEA.

1.  Flame Temperature Calculations with Full Chemical Equilibrium

Thus far, we have learned how to calculate adiabatic flame temperature assuming complete combustion and only saturated products.  Then we learned how to calculate the actual products of combustion, given the final temperature and pressure.  Now, we can combine the two concepts to learn how to calculate adiabatic flame temperature and the actual combustion products simultaneously.

Example 3.1

Known: Ethane is burned stoichiometrically with air in a Bunsen burner. T1 = 298 K.

Find: The final product distribution (molar flow rates and mole fractions) and the final temperature, T2.

In general, we can use all of the information we have learned so far.  In fact we can formulate the problem already using our experience:

(n3.1)

But now, unlike in the TP case, the final temperature T2 is unknown!  Since we have one more unknown, we need one more equation.  What equation can we use?

Constructing a control volume around the Bunsen burner:

We can formulate the First Law of Thermodynamics on a molar basis for this control volume:

(n3.2)

Substituting the total enthalpy into the above equation yields:

(n3.3)

Since, in our example, the inlet temperature was 298 K, the enthalpy difference terms are all zero.  Furthermore, the Heat of Formation terms for Nitrogen, and Oxygen are also zero. Canceling out these terms yields the following equation:

(n3.4)

Recalling that the sensible enthalpy is related to the specific heat, we can substitute these relationships into the above equation:

(n3.5)

Finally, recall that we postulated the following products to be present at equilibrium:

N2, CO2, H2O, OH, CO, O2 and H2

Substituting, results in the final equation needed to solve the problem:

(n3.6)

The energy equation can be solved along with the conservation of element equations and Kp equations (n3.3) to determine the molar quantities of each component and the adiabatic flame temperature, T2.

Some notes on the above equation:

- Note how much of the energy goes into heating the nitrogen.  For every 1 mole of oxygen burned, we have to heat up 3.76 moles of nitrogen.

- In general, the reactants will not be entering the flame at 298 K, so the left hand side of the equation might be more complicated.

- We ignored species such as NO.

Solution Scheme:

So, how do we solve this problem?  Generally, we have to solve it iteratively, just like the TP problem.  Here is one scheme:

1.   Guess a T2.

2.   Use the guessed T2 value to evaluate all of the Kp’s at T2.

3.   Iterate through the element conservation and Kp equations until they converge to solve for all of the molar quantities, ni.

4.   Plug the predicted molar quantities into the energy equation and see if the energy equation is satisfied.  If not, go to step 1.

2. Computer Models for Equilibrium Calculations

As you know from HW #3, equilibrium calculations are difficult enough by hand, even if you know the final temperature, T2.  Solving for the adiabatic flame temperature using equations (n3.1) and (n3.6), for example, is even more difficult.  Fortunately, there are a variety of computer programs that you can use to solve these problems.  Example programs are as follows:

After you have done an equilibrium calculation or two, you are now well qualified to use a computer code to calculate the answers for you.  It is still a good idea to set up the problem by hand, though, because the "Art of Equilibrium" still applies.  In other words, if you do not set up the problem, you will have no idea if the answers that the code gives you are reasonable.

When using scientific and engineering computer codes, remember the saying, "garbage in…garbage out!"

2.1 The NASA CEA Computer Code

The NASA CEA Computer Code is available for download from the course web site:

http://www.engr.colostate.edu/~marchese/combustion08/cec.htm

It can be copied (along with several required data files) directly to your hard drive.  It runs in a .dos shell.  The executable is named cea300.exe

A web based version of the code is now also available at NASA’s website:

http://cearun.grc.nasa.gov/index.html

The NASA CEA code can be used to solve the Temperature-Pressure problem and the adiabatic flame temperature problem.

Example 3.2.  The NOx problem revisited.

Air is heated to 2000K at 1 atm.  What are the mole fractions (ppm) of NO and NO2 present at equilibrium?

The following input data set was supplied to the CEA program:

problem  tp  equilibrium

p,psia=14.7 t(k)=2000.0

reactants

fuel = N2 moles=0.79

oxid = O2 moles=0.21

output  siunits

end

The NASA CEA code predicted the following equilibrium mole fractions:

*******************************************************************************

NASA-LEWIS CHEMICAL EQUILIBRIUM PROGRAM CEA,  APR. 28, 1997

BY  BONNIE MCBRIDE AND SANFORD GORDON

REFS: NASA RP-1311, PART I, 1994 AND NASA RP-1311, PART II, 1996

*******************************************************************************

THERMODYNAMIC EQUILIBRIUM PROPERTIES AT ASSIGNED

TEMPERATURE AND PRESSURE

REACTANT                       MOLES         ENERGY      TEMP

KJ/KG-MOL      K

FUEL        N2                            .7900000          .000       .000

OXIDANT     O2                            .2100000          .000       .000

O/F=     .30364  %FUEL= 76.708300  R,EQ.RATIO=  .000000  PHI,EQ.RATIO=  .000000

THERMODYNAMIC PROPERTIES

P, BAR            1.0135

T, K             2000.00

RHO, KG/CU M    1.7582-1

H, KJ/KG         1994.80

U, KJ/KG         1418.33

G, KJ/KG        -16042.7

S, KJ/(KG)(K)     9.0187

M, (1/n)          28.846

(dLV/dLP)t      -1.00008

(dLV/dLT)p        1.0023

Cp, KJ/(KG)(K)    1.3457

GAMMAs            1.2740

SON VEL,M/SEC      857.0

MOLE FRACTIONS

*NO               .00758

NO2               .00001

*N2               .78609

*O                .00030

*O2               .20602

* THERMODYNAMIC PROPERTIES FITTED TO 20000.K

PRODUCTS WHICH WERE CONSIDERED BUT WHOSE MOLE FRACTIONS

WERE LESS THAN 5.000000E-06 FOR ALL ASSIGNED CONDITIONS

*N              NO3             N2O             N2O3            N2O4

N2O5            N3              O3

Note:  Our calculations were pretty good.  We should have included O atom.

Example 3.3. Adiabatic Flame Temperature

Ethane and air are burned stoichiometrically in a bunsen burner at 1 Atm.  Assuming no heat loss, what are the final temperature and mole fractions?

The following input data set was supplied to the CEA program:

problem  hp  equilibrium

p,psia=14.7

reactants

fuel = C2H6 moles=1 t(k)=298

oxid = O2 moles=3.5 t(k)=298

oxid = N2 moles=13.16 t(K)=298

output  siunits

end

The code predicted the following:

*******************************************************************************

NASA-LEWIS CHEMICAL EQUILIBRIUM PROGRAM CEA,  APR. 28, 1997

BY  BONNIE MCBRIDE AND SANFORD GORDON

REFS: NASA RP-1311, PART I, 1994 AND NASA RP-1311, PART II, 1996

*******************************************************************************

THERMODYNAMIC EQUILIBRIUM COMBUSTION PROPERTIES AT ASSIGNED

PRESSURES

REACTANT                       MOLES         ENERGY      TEMP

KJ/KG-MOL      K

FUEL        C2H6                         1.0000000    -83859.418    298.000

OXIDANT     O2                           3.5000000        -4.407    298.000

OXIDANT     N2                          13.1600000        -4.369    298.000

O/F=   15.98467  %FUEL=  5.887663  R,EQ.RATIO= 1.000000  PHI,EQ.RATIO= 1.000000

THERMODYNAMIC PROPERTIES

P, BAR            1.0135

T, K             2259.12

RHO, KG/CU M    1.5041-1

H, KJ/KG         -164.34

U, KJ/KG         -838.16

G, KJ/KG        -22203.3

S, KJ/(KG)(K)     9.7556

M, (1/n)          27.876

(dLV/dLP)t      -1.00289

(dLV/dLT)p        1.0855

Cp, KJ/(KG)(K)    2.2601

GAMMAs            1.1801

SON VEL,M/SEC      891.7

MOLE FRACTIONS

*CO               .01159

*CO2              .09757

*H                .00046

*H2               .00344

H2O               .15848

*NO               .00224

*N2               .71718

*O                .00029

*OH               .00318

*O2               .00557

Note(s):

- Adiabatic flame temperature is 2259 K.

- Lots of CO (11590 ppm) and NO (2240 ppm) predicted.  Yikes!  We should all be dead!

Summary.  You now know how to solve any chemical equilibrium problem!

- The TP Problem.

- The Flame Temperature Problem (both adiabatic and non-adiabatic!).