## Slide 1
Alyssa Aligata
Mechanical Engineering Graduate Student
Biofuels from Microalgae
October 2, 2017
KEY 192A

## Slide 2
Algal Biofuels: Progress and Research Challenges
Overview
  Motivation for Renewable Liquid Fuels
  The Case for Algae
  Current Research Challenges: Biology to Combustion
  Cultivation, Harvesting and Extraction Research
  Conversion of Algal Lipids and Biomass into Liquid Fuels
  Conclusions

## Slide 3
Algal Biofuels: Progress and Research Challenges
Overview
  Motivation for Renewable Liquid Fuels
  The Case for Algae
  Current Research Challenges: Biology to Combustion
  Cultivation, Harvesting and Extraction Research
  Conversion of Algal Lipids and Biomass into Liquid Fuels
  Conclusions

## Slide 4: Biofuels Introduction
Biofuel = liquid fuel that has been developed from renewable plant or animal materials
Why are biofuels important?
  Finite fossil fuels
  Carbon footprint
  Energy security

## Slide 5: Algal Biofuels

## Slide 6
Algal Biofuels: Progress and Research Challenges
Overview
  Motivation for Renewable Liquid Fuels
  The Case for Algae
  Current Research Challenges: Biology to Combustion
  Cultivation, Harvesting and Extraction Research
  Conversion of Algal Lipids and Biomass into Liquid Fuels
  Conclusions

## Slide 7: Life Cycle Assessment
Technique to assess environmental impacts associated with all the stages of a product's life from raw material extraction through materials processing, manufacture, distribution, use, repair and maintenance, and disposal or recycling

## Slide 8
Advanced Biofuels
Offer Significant Reduction in Greenhouse Gas Emissions

## Slide 9
U.S. Advanced Biofuels Mandate
21 billion gal/year by 2022
  The 2007 Energy Independence and Security Act (EISA) mandates the production of 36 billion gallons per year of biofuels by 2022
    21 billion gallons per year must qualify as advanced biofuels.
  Note: the U.S. consumes 300 Billion gallons per year of liquid fuels

## Slide 10
The Case for Algae
Phototrophic Microalgae is Potentially Scalable
  21 billion gallons per year of “advanced biofuels” ≈ 10% of U.S. liquid on-road fuel usage ≈ how much cultivation area?
21 billion gallons per year of soy biodiesel (≈ Alaska)
21 billion gallons per year of algae biodiesel (≈ Connecticut)

## Slide 11
Algal Biofuels: Progress and Research Challenges
Overview
  Motivation for Renewable Liquid Fuels
  The Case for Algae
  Current Research Challenges: Biology to Combustion
  Cultivation, Harvesting and Extraction Research
  Conversion of Algal Lipids and Biomass into Liquid Fuels
  Conclusions

## Slide 12: Current Research Challenges Biology, Cultivation, Harvesting, Extraction, Conversion, Co-Products
Biology
Cultivation
Harvesting
Extraction
Conversion
Co-products

## Slide 13: Current Research Challenges Direct Conversion of Wet Algae Biomass into Bio-Crude Oil
Biology
Cultivation
Harvesting
Whole Algal Biomass
Conversion to Biocrude
Upgrading to
Drop-In Fuels
Nutrient Recycle

## Slide 14
Algal Biofuels: Progress and Research Challenges
Overview
  Motivation for Renewable Liquid Fuels
  The Case for Algae
  Current Research Challenges: Biology to Combustion
  Cultivation, Harvesting and Extraction Research
  Conversion of Algal Lipids and Biomass into Liquid Fuels
  Algal Biofuel Combustion and Engines Research
  Conclusions

## Slide 15: Cultivation Research: Open Ponds
Numerous profitable enterprises use open pond cultivation techniques for high value products (e.g. pharmaceutical)
Advantages
Lowest capital cost
Only technology demonstrated to date at large scale
Research Issues
Contamination of specific culture with local species
Susceptible to weather , dust, sand
Water loss from evaporation
Unconfined genetically modified organisms is a concern for many!
Earthrise, California
Nutrex, Hawaii

## Slide 16: Cultivation Research: Closed PhotoBioreactors
Advantages
Allow growth of specific cultures
No contamination from invasive species
Allows environmental control
Potential for much higher growth rates
Ability to confine GMO’s
Disadvantages
Higher capital cost
Higher energy costs
Low-cost production has not been demonstrated
Glass Plate Photobioreactor (Pulz, Richmond, others)
Glass Tube Photobioreactor (Pulz, IGV, Ketura, Torzillo, others)

## Slide 17: Solix BioSystems Development of Low Cost Scalable PhotoBioreactors
Solix G3 Technology:
Extended surface area
Water supported
Integrated CO2 / air sparging

## Slide 18
18
Full Scale Demonstration Site
Approximately 1 acre surface area.

## Slide 19
Approximately 1 acre surface area
Solix Full Scale Demonstration Site

## Slide 20: Open Pond Cultivation at Scale
Earthrise, California
Location: Columbus, NM
Feedstock(s): CO2/Algae/Sunlight/Non-Potable Water
Size: 300 acres of open raceway ponds
Primary Products: Jet fuel and diesel
Capacity: 1 million gallons per year of finished product
Operations: Phase 1 - 100 acres of ponds; Phase 2 - scale up and expand farming operations.

## Slide 21: Constraints for Scale Up to 21 Billion gal/year in U.S.
Technoeconomic study completed by CSU to evaluate U.S. resources available to achieve EISA 21 billion gal/year from algae alone
Model: N. salina, PBR growth, centrifugal dewater, ethanol/ hexane lipid extraction, validated microalgae growth models, GIS data
What resources will limit microalgae productivity?
  1. Climate, sunlight, temp
  2. Land availability, slope
  3. CO2 availability (within a constraint of 5km)
Results:
Suitable land for algae production would yield
only 1 billion gal/year with
these constraints.
Quinn, J. and Bradley, T. (2013).

## Slide 22: Microalgae Cultivation Research Environmental Impacts of Microalgae Cultivation
Nitrous oxide (N2O) has 300 times the global warming potential of CO2.
The goal of this study was to measure N2O emissions during cultivation.
Direct measurement showed that emissions were minimal, except for under conditions of low light and low dissolved oxygen.
Fagerstone, K., Quinn, J. C., De Long, S, Bradley, T. and Marchese, A. J. (2011). Quantitative Measurements of Direct N2O Emissions from Microalgae Cultivation. Environmental Science & Technology 45 (21), pp. 9449-9456.

## Slide 23: Harvesting Microalgae
Need to collect the algae and remove water
Common methods:
These methods are energy intensive and expensive!
Centrifugation
Flocculation
Filtration

## Slide 24: Microalgae Harvesting Research
Acoustic Radiation Force, Fac, acting on particles of radius, R, in a liquid media subjected to a ultrasonic standing wave:
Hincapie and Marchese (2014). An Ultrasonically Enhanced Inclined Settler for Microalgae Harvesting. Biotechnol. Prog. DO 10.1002/btpr.2031
Ultrasonic techniques represent a low-energy, scalable solution.
Ultrasonic Harvesting of Microalgae
cp / cm

## Slide 25: Microalgae Harvesting Research
Acoustic Radiation Force, Fac, acting on particles of radius, R, in a liquid media subjected to a ultrasonic standing wave:
Hincapie and Marchese (2014). An Ultrasonically Enhanced Inclined Settler for Microalgae Harvesting. Biotechnol. Prog. DO 10.1002/btpr.2031
Ultrasonic techniques represent a low-energy, scalable solution.
Ultrasonic Harvesting of Microalgae
cp / cm

## Slide 26: Microalgae Harvesting Research
Acoustic Radiation Force, Fac, acting on particles of radius, R, in a liquid media subjected to a ultrasonic standing wave:
Hincapie and Marchese (2014). An Ultrasonically Enhanced Inclined Settler for Microalgae Harvesting. Biotechnol. Prog. DO 10.1002/btpr.2031
Ultrasonic techniques represent a low-energy, scalable solution.
Ultrasonic Harvesting of Microalgae
cp / cm

## Slide 27: Microalgae Harvesting Research

## Slide 28: Microalgae Harvesting Research
Uses standing waves to separate out particles in suspension with a liquid
Piezoelectric disc creates standing wave
Standing wave exerts a force on the particles and pushes them into lines

## Slide 29: Ultrasonic Microalgae Harvesting Development of a Continuous Flow System
Hincapie and Marchese (2014). An Ultrasonically Enhanced Inclined Settler for Microalgae Harvesting. Biotechnol. Prog. DO 10.1002/btpr.2031

## Slide 30: Microalgae Harvesting Research
Camera
Cuvette with Piezo
Microscope
Before
After
Record particle / cell movement

## Slide 31: Microalgae Harvesting Research
Cells are made of lipids, carbohydrates, and proteins
  Each component has different acoustic properties
Cell composition affects the ability to harvest with acoustics
cp / cm

## Slide 32: Acoustic Harvesting Device

## Slide 33: Acoustic Harvesting Device

## Slide 34: Acoustic Harvesting Setup
Acoustic Harvester
Small Amplifier
Large Amplifier
Oscilloscope
Function Generator

## Slide 35
Algal Biofuels: Progress and Research Challenges
Overview
  Motivation for Renewable Liquid Fuels
  The Case for Algae
  Current Research Challenges: Biology to Combustion
  Cultivation, Harvesting and Extraction Research
  Conversion of Algal Lipids and Biomass into Liquid Fuels
  Conclusions

## Slide 36: The Algae Biofuels Value Chain The “Conventional” Route: Extracted Lipids to Fuel
Biology
Cultivation
Harvesting, Drying?
Lipid Extraction
Lipid to Fuel Conversion
Co-products
Nutrient Recycle

## Slide 37: Conversion of Algal Lipids into Liquid Fuels Algal Renewable Diesel/Jet Fuel

## Slide 38: Conversion of Algal Lipids into Liquid Fuels Algal Renewable Diesel/Jet Fuel

## Slide 39: The Algae Biofuels Value Chain (Revisited) Conversion of Whole (Wet) Algal Biomass To Biofuels
Biology
Cultivation
Harvesting
Whole Wet Algal Biomass
Conversion to Biocrude
Upgrading to
Drop-In Fuels
Nutrient Recycle

## Slide 40: Conversion of Whole Algal Biomass into Fuels Hydrothermal Liquefaction (HTL)
Hydrothermal liquefaction uses water at sufficient temperature and pressure to convert a wet biomass feedstock directly into a liquid bio-crude oil.
By processing the feedstock wet, the need for drying is eliminated.
Process temperatures are lower compared to dry pyrolysis.
  Current process conditions for the continuous flow system at PNNL are just below the supercritical point of water (350⁰C, 3000 psi).
Feedstock: Wet Nannochloropsis salina Paste
HTL Bio-Oil
Hydrotreated HTL Bio-Oil
Fractionated cuts: naphtha, diesel, bottoms
Elliott, D. and Oyler, J. (2012). Hydrothermal processing: Efficient production of high-quality fuels from algae. 2nd International Conference on Algal Biomass, Biofuels and Bioproducts, San Diego, CA, June 2012.

## Slide 41
Algal Biofuels: Progress and Research Challenges
Overview
  Motivation for Renewable Liquid Fuels
  The Case for Algae
  Current Research Challenges: Biology to Combustion
  Cultivation, Harvesting and Extraction Research
  Conversion of Algal Lipids and Biomass into Liquid Fuels
  Conclusions

## Slide 42: Conclusions
Microalgae is a potentially scalable liquid biofuel
  The “ambitious” goal is 36 billion gal/year by 2022
  300 billion gal/year will be needed in future generations
Many challenges remain to realize commercial viability at scale
  biological challenges, engineering challenges, economic challenges
Acoustic harvesting could lower the overall energy requirements and cost of algal fuel

## Slide 43
Questions?