Homework Assignment Due: Wednesday, 2/25/15

1. Mercury Redstone Rocket.  The Redstone rocket was used to put the United State’s first man in space.  The flight was a 15 minute, sub-orbital flight with an altitude of 186,400 m.  The Redstone rocket was powered by a single A-7 rocket engine which burned a mixture of ethanol and water with liquid oxygen at a chamber pressure of 320 psia.  The total mass flow rate was 155 kg/s, the nozzle exit pressure was 5 psia and the nozzle area ratio (Ae/At) was 10.

Based on thermodynamic calculations, this propellant combination results in the following: Tc = 3200 K,  = 1.12, MW = 23.6 g/mol.

Calculate:

a) C*

b) At

c) CF at sea level

d) Specific Impulse at sea level

e) Thrust at sea level

f) CF at 10,000 m

g) Specific impulse at 10,000 m

h) Thrust at 10,000 m

2.  NASA 1 kW Arcjet.  Calculate the c*, , Isp and thrust for a 1 kW class Arcjet operating on Helium, Hydrogen (H2) and Hydrazine (N2H4).   Assume the following parameters are the same for each propellants: Pc = 50 psia, Pa = 0.2 Torr, Ae/At = 150, dt = 0.64 mm, Tc = 5000 K

The following thermodynamic calculations were performed for each of the three propellants:

|  | He | H2 | N2H4 |
| --- | --- | --- | --- |
| Tc | 5000 K | 5000 K | 5000 K |
| Pc | 50 psia | 50 psia | 50 psia |
| Species mole fractions present at Tc, Pc | He 1.0000 | H 0.92836 H2 0.07164 | H .74177 H2 .04573 N .00806 NH .00021 N2 .20422 |
|  | 1.6667 | 1.2755 | 1.2548 |

3.  Hybrid Rocket Motor Design Project.  From thermodynamic calculations, we know that the optimum performance of an HTPB/GOX hybrid rocket engine will occur at an O/F ratio of 2.0.  At this O/F ratio, the C* and  were calculated to be 5912 ft/s and 1.152, respectively. Due to safety considerations, we will be constrained to a chamber pressure of 200 psig and we will be operating our rocket motor at sea level, but we should design for an exit pressure of 5 psia.  The desired thrust is 10 lbf.

Calculate:  Ae/At, CF at sea level, At, dt (inches), de (inches), total mass flow rate (kg/s), reguired oxygen mass flow rate (kg/s), Isp.