- Relationship between nozzle area ratio and pressure ratio.

Recalling the equation for thrust coefficient (37), we see that the first term is a function only of the nozzle pressure ratio and the second term is a function of the atmospheric pressure.  The first term, CFo, is a constant for a given area ratio nozzle since, for a supersonic nozzle, the nozzle pressure ratio is a function of the nozzle area ratio:

(37)

Note:  In designing a rocket, we are given Pc and Pa as main design parameters.  The desired goal is to design a nozzle such that the exit pressure, Pe, closely matches the ambient pressure Pa.  Obviously, this is not always possible.

To design a nozzle that achieve a given exit pressure, we need to determine the relationship between pressure ratio and area ratio in a nozzle.  Consider the following nozzle.

Nozzle Area Ratio  				Nozzle Pressure Ratio

To derive a relationship between area ratio and pressure ratio, we start with the continuity equation, and solve for the area ratio:

(1)

Recalling the isentropic relationships for T/To, /o, P/Po and a/ao vs. Mach #:

Substituting (using the isentropic relationships and substituting M=1 at the throat):

Results in the following:

(2)

Note:  The nozzle area ratio is not a function of propellant energetics (RTc), just the ratio of exit pressure to chamber pressure!

This is a key equation, since it allows us to design the nozzle area ratio given parameters that we generally know something about:  Pc and Pe.  The latter pressure, we would like to be as close as possible to Pa.

- Relationship between nozzle area ratio and Mach #:

You can also start with the continuity equation to derive an expression for area vs. Mach number:

Substituting the isentropic relationships for M=1 at the throat and M=Me at the exit yields:

3)

- Using thrust coefficient, area ratio, and Mach # equations to design a rocket nozzle

Rocket scientist have been using the above equations for rocket design for a long time.  For example, Fig. 3.6 in Sutton is a plot of the CFo vs. pressure ratio for various :

And figure 3.4 and 3.5 in Sutton is a plot of Area ratio vs. pressure ratio for various .

Note:  As a first guess, you should use  = 1.2 for rocket exhaust gases.  The NASA CEC code will calculate a  for you.

Example 4.1: How to use the above graphs and/or equations.

Known:  A rocket nozzle needs to be designed optimally for the following conditions.

Find:  The nozzle area ratio and the rocket thrust as a function of nozzle exit area.

Given:  Pc = 70 Atm.  Pe = 1 atm.   = 1.2.

Example 4.2 Basic Example for the Design of a Rocket

We now have the basic theory that we need to start the conceptual design of a rocket engine.  A similar procedure can be used in your semester design project.

Known:  A rocket needs to be designed for horizontal flight at 10,000 meters.  The rocket must generate 100,000 N of thrust for 5 seconds.

Find: Nozzle area ratio, mass flow rate, mass of propellant, thrust coefficient, Isp, Total Impulse, throat diameter, nozzle exit diameter, Chamber temperature and Sea Level Thrust.

Given:  Cstar = 1500 m/s,  = 1.2, MW = 25 kg/kmol, Pc = 1000 psia, tb = 5 sec.

(Note: these are typical values that a rocket designer will start with, if a propellant combination has not been decided on yet, or if the exact performance of a propellant combination is not yet known.)

Design Example (Continued)

- Designing an Optimum Nozzle for Varying Ambient and/or Chamber Pressure

In the previous example, the rocket traveled horizontally at 10,000 meters and the chamber pressure was constant at 1000 psia.  Therefore, it was possible to design a rocket nozzle so that the exit pressure was identically equal to the ambient pressure.

We then found that if that same rocket were fired at sea level, the thrust would decrease from 100,000 N to 80,000 N.

How would you design an optimum nozzle if the chamber pressure and/or the ambient pressure varied as follows?

You can use the following equation:

The following table contains atmospherica pressure, temperture, density, acceleration due to gravity, viscosity, thermal conductivity and speed of sound as a function of altitude.