## Slide 1
Anthony J. Marchese
Associate Prof. and Associate Dept. Head
Department of Mechanical Engineering
Colorado State University
http://www.engr.colostate.edu/~marchese
Fuel Properties and Pollutant Emissions from Algal Biodiesel, Algal Renewable Diesel and Algal HTL Fuels
Sustainable Bioenergy Development Center - Bioenergy at CSU Seminar
October 16, 2012

## Slide 2: Acknowledgments Advanced Biofuels Combustion and Characterization Laboratory
Graduate Students:
  Caleb Elwell
  Timothy Vaughn
  Torben Grumstrup
  David Martinez
  Esteban Hincapie
  Kristen Naber
  Marc Baumgardner
  Jessica Tryner
  Andrew Hockett
  Harrison Bucy, ‘11
  Kelly Fagerstone, ’11
  Bethany Fisher, ‘10
  Anthony
  Dave
  David
  Tim
  Harrison
  Kelly
  Torben
  Marc
  Esteban
  Kristen
  Bethany
  Andrew
  Jessica

## Slide 3
Review Algal Biofuels Conversion Technologies
Overview
  Motivation for Algal Biofuels
  The Algal Biofuel Value Chain Revisited
  Algal Methyl Ester Biodiesel Properties
  Algal Synthetic Paraffinic Diesel/Jet Fuel Properties
  Algal Hydrothermal Liquefaction Oil Properties
  Conclusions

## Slide 4
Review Algal Biofuels Conversion Technologies
Overview
  Motivation for Algal Biofuels
  The Algal Biofuel Value Chain Revisited
  Algal Methyl Ester Biodiesel Properties
  Algal Synthetic Paraffinic Diesel/Jet Fuel Properties
  Algal Hydrothermal Liquefaction Oil Properties
  Conclusions

## Slide 5
Peak Oil
Are we there yet?
The End of the Oil Age?

## Slide 6
Peak Oil
Anomalous Age of Easy Oil is Nearing its End

## Slide 7
Campbell, C. J. (2012). The Anomalous Age of Easy Energy. Energy, Transport and the Environment, Springer.
Peak Oil
Anomalous Age of Easy Oil is Nearing its End

## Slide 8
FFC/GDP is fundamentally constrained by the 2nd Law of Thermodynamics!
The Master Equation
Fossil Fuel Depletion (A Matter of WHEN…not IF)

## Slide 9
Non-Conventional Liquid Fossil Fuels
Substantial Resources Still Exist for GTL or CTL
Enhanced oil recovery
Potential Liquid Hydrocarbon Production (Gbbl)

## Slide 10: Keeling Curve, CO2 at Mauna Loa
Non-Conventional Liquid Fossil Fuels
Do We Really Want to Release All of That Carbon?

## Slide 11
U.S. Advanced Biofuels Mandate
21 billion gal/year by 2022
  The United States typically consumes 300 Billion gallons per year of liquid fuels:
    130 Billion gal/year gasoline, 70 Billion gal/year diesel, 24 Billion gal/year jet fuel
  The 2007 Energy Independence and Security Act (EISA) mandates the production of 36 billion gallons per year of biofuels by 2022
    Corn ethanol is capped at 15 billion gallons per year.
    21 billion gallons per year must qualify as advanced biofuels.
  Can Algal Biofuels help meet the advanced biofuels mandate?

## Slide 12
The Case for Algae
  21 billion gallons per year of “advanced biofuels” ≈ 10% of U.S. liquid on-road fuel usage ≈ how much cultivation area?
21 billion gallons per year of soy biodiesel (≈ Alaska)
21 billion gallons per year of algae biodiesel (≈ Connecticut)

## Slide 13
Review Algal Biofuels Conversion Technologies
Overview
  Motivation for Algal Biofuels
  The Algal Biofuel Value Chain Revisited
  Algal Methyl Ester Biodiesel Properties
  Algal Synthetic Paraffinic Diesel/Jet Fuel Properties
  Algal Hydrothermal Liquefaction Oil Properties
  Conclusions

## Slide 14
Review Algal Biofuels Conversion Technologies
Overview
  Motivation for Algal Biofuels
  The Algal Biofuel Value Chain Revisited
  Algal Methyl Ester Biodiesel Properties
  Algal Synthetic Paraffinic Diesel/Jet Fuel Properties
  Algal Hydrothermal Liquefaction Oil Properties
  Conclusions

## Slide 15: The Algal Biofuels Value Chain The “Conventional” Route
Biology
Cultivation
Harvesting, Drying?
Lipid Extraction
Lipid to Fuel Conversion
Co-products
Nutrient Recycle

## Slide 16: The Algal Biofuels Value Chain Conversion of Whole Algal Biomass To Biofuels via HTL
Biology
Cultivation
Harvesting
Whole Wet Algal Biomass
Conversion to Biocrude
Upgrading to
Drop-In Fuels
Nutrient Recycle

## Slide 17
Review Algal Biofuels Conversion Technologies
Overview
  Motivation for Algal Biofuels
  The Algal Biofuel Value Chain Revisited
  Algal Methyl Ester Biodiesel Properties
  Algal Synthetic Paraffinic Diesel/Jet Fuel Properties
  Algal Hydrothermal Liquefaction Oil Properties
  Conclusions

## Slide 18
Review Algal Biofuels Conversion Technologies
Overview
  Motivation for Algal Biofuels
  The Algal Biofuel Value Chain Revisited
  Algal Methyl Ester Biodiesel Properties
  Algal Synthetic Paraffinic Diesel/Jet Fuel Properties
  Algal Hydrothermal Liquefaction Oil Properties
  Conclusions

## Slide 19: Conversion of Algal Lipids into Liquid Fuels Algal Paraffinic Renewable Diesel vs. Algal Biodiesel
Algal Biodiesel
Alkyl esters produced via trans-esterification of TAG’s:
Fuel properties are directly related to fatty acid composition of TAG’s.
Processing susceptible to contaminants (P, S, Ca, Mg, K, etc.) and FFA’s
Only suitable for diesel engines
Small to moderate scale processing facilities ( < 100 million gal/year)
Current U.S. production capacity (3 billion gal/year) is under utilized.
Currently feedstock limited
Algal Renewable Diesel
Straight and branched alkanes:
Processing requirements and fuel properties are relatively agnostic to fatty acid composition of TAG’s
Processing is susceptible to contaminants (P, S, Ca, Mg, K, etc.)
Final products compatible with existing refinery and distribution infrastructure
Properties can be tailored for gasoline, diesel, or jet fuel (ASTM D7566-11)
Large scale processing facilities are favored ( >100 million gal/year)
Currently feedstock limited

## Slide 20
Conversion of Algal Lipids to Fuels
Algal Methyl Ester Biodiesel
Fatty acid profiles of some extracted algal lipids differ from that of conventional biodiesel feedstocks.
For algal FAME, the fatty acid profile has implications in terms of oxidative stability, cold temperature properties, ignition quality and engine emissions.
 | 8:0 | 10:0 | 12:0 | 14:0 | 16:0 | 16:1 | 18:0 | 18:1 | 18:2 | 18:3 | 20:1 | 20:4 | 20:5 | 22:6
Soy |  |  |  |  | 11 |  | 4 | 24 | 53 | 8 |  |  |  | 
Jatropha |  |  |  |  | 11 |  | 17 | 13 | 47 | 0 | 5 |  |  | 
Coconut | 8 | 6 | 47 | 18 | 9 |  | 3 | 7 | 2 |  |  |  |  | 
Palm |  |  |  | 1 | 39 |  | 5 | 46 |  | 9 |  |  |  | 
Nannochloropsis salina |  |  |  | 3 | 30 | 39 | 1 | 8 | 1 | 1 |  | 3 | 11 | 
Nannochloropsis oculata |  |  |  | 2 | 15 | 16 | 2 | 10 | 4 | 3 |  | 6 | 21 | 3
Isoschrysis galbana |  |  |  | 23 | 14 | 3 | 1 | 14 | 5 | 7 |  |  | 5 | 14
Bucy, H., Baumgardner, M. and Marchese, A. J. (2012). Chemical and Physical Properties of Algal Methyl Ester Biodiesel Containing Varying Levels of Methyl Eicosapentaenoate and Methyl Docosahexaenoate. Algal Research 1 pp. 57–69.

## Slide 21: Oxidative Stability of Algal Methyl Esters Effect of EPA and DHA
O-O-H
●
O-O
+O2
●
In natural oils, multiple olefinic unsaturation occurs in a methylene- interrupted configuration. The bis-allylic C-H bonds are susceptible to hydrogen abstraction, followed by oxygen addition, and peroxide formation
Fuels containing long chain unsaturated methyl esters such as EPA (C20:5) and DHA (C22:6) have poor oxidative stability.

## Slide 22: Oxidative Stability of FAME Bis-Allylic Position Equivalents (BAPE) (Knothe and Dunn, 2003)
Oxidative stability of FAME has been shown to correlate with the total number of bis-allylic sites in the FAME blend.
To capture this effect, Knothe and Dunn (2003) have defined Bis-Allylic Position Equivalents (BAPE) parameter, which is a weighted average of the total number of bis-allylic sites in the FAME mixture:
For the present work, model algal methyl ester compounds were formulated to match the BAPE value of real algal methyl esters subject to varying levels of EPA/DHA removal.
bis-allylic sites

## Slide 23: Oxidative Stability Tests Metrohm 743 RANCIMAT Test
Instrument | Method Followed | Standard | Specification | Test Parameters |  | 
Metrohm 743Rancimat | EN 14112 | D6751 | 3 hours minimum | 10 L/h air flow | 110°C | 3 gram sample
 |  | EN 14214 | 6 hours minimum |  |  | 

## Slide 24: Oxidative Stability Tests Metrohm 743 RANCIMAT Test
Instrument | Method Followed | Standard | Specification | Test Parameters |  | 
Metrohm 743Rancimat | EN 14112 | D6751 | 3 hours minimum | 10 L/h air flow | 110°C | 3 gram sample
 |  | EN 14214 | 6 hours minimum |  |  | 

## Slide 25: Oxidative Stability Test Results Model Compounds and Real Algal Methyl Esters Correlate with BAPE

## Slide 26: Oxidative Stability Effect of EPA/DHA Removal from Nannochloropsis oculata
Bucy, H., Baumgardner, M. and Marchese, A. J. (2012). Chemical and Physical Properties of Algal Methyl Ester Biodiesel Containing Varying Levels of Methyl Eicosapentaenoate and Methyl Docosahexaenoate. Algal Research 1 pp. 57–69.

## Slide 27: Oxidative Stability Test Results Effect of TBHQ Oxidative Stability Additive
The effect of adding an oxidative stability additive (Vitablend Bioprotect 350) is shown here. Active ingredient: tert-Butylhydroquinone (TBHQ))

## Slide 28: Ignition Quality Tests Derived Cetane Number Tests with Waukesha FIT System
ASTM D7170 Method
  Measures ignition delay of 25 injections into a fixed volume combustor
  DCN = 171/ID
Instrument | Method | Standard | Specification | Test Parameters |  |  | 
 |  |  |  | # of Injections | Injection Period | Fuel Temperature | Coolant Temperature
Waukesha FIT | D7170 | D6751 | 47 minimum | 25 injections | 5.00+/-0.25 ms | 35+/-2°C | 30+/-0.5°C
Cetane Number is a measure of the propensity for a liquid fuel to auto-ignite under diesel engine conditions. For biodiesel a minimum Cetane Number of 47 is required.

## Slide 29: Cetane Number Effect of EPA/DHA Removal from Nannochloropsis oculata
Nannochloropsis and Isochrysis galbana based algal methyl esters were shown to have lower than acceptable Cetane Number.
As EPA and DHA are removed, Cetane Number increases.
Bucy, H., Baumgardner, M. and Marchese, A. J. (2012). Chemical and Physical Properties of Algal Methyl Ester Biodiesel Containing Varying Levels of Methyl Eicosapentaenoate and Methyl Docosahexaenoate. Algal Research 1 pp. 57–69.

## Slide 30: Cloud Point and Cold Filter Plugging Point
Removal of C20:5 and C22:6 from algal methyl esters also results in an increase in the percentage of fully saturated methyl esters C16:0 and C18:0, resulting in increased cloud point and cold filter plugging point.

## Slide 31: Cloud Point and Cold Filter Plugging Point
Removal of C20:5 and C22:6 from algal methyl esters also results in an increase in the percentage of fully saturated methyl esters C16:0 and C18:0, resulting in increased cloud point and cold filter plugging point.

## Slide 32: Speed of Sound and Bulk Modulus
Increased bulk modulus of FAME (in comparison to petroleum diesel) results in advanced injection timing and increased NOx.
Speed of sound (a) and bulk modulus (a2r) of the liquid FAME formulations also correlated well with BAPE.

## Slide 33
Objective: Characterize PM size distribution /composition and gaseous pollutants from algae-based methyl esters.
Approach: Engine tests were performed on a 52 HP John Deere 4024T diesel engine at rated speed at 50% and 75% of maximum load.
Fuels: Fuels tested include ULSD, soy methyl ester, canola methyl ester, and two model algal methyl ester compounds:
  Nannochloropsis oculata and Isochrysis galbana methyl ester compounds.
  B20 and B100 blends of each methyl ester were tested.
  Nine fuel blends tested in total
Emissions Testing (Fisher et al., 2010)
Characterization of PM and NOx from Algae Based Methyl Esters

## Slide 34: Hydrocarbon and CO Emissions
Emissions of CO and THC for the algal methyl esters were similar to that of the soy and canola methyl esters, which were similar to that reported in the literature.
Total Hydrocarbons
Carbon Monoxide

## Slide 35
NOx Emissions from Diesel Engines
Nannochloropsis Methyl Ester Model Compounds
Emissions of NOx were shown to decrease for the algal methyl esters in comparison to the ULSD, in contrast to the soy and canola methyl esters which resulted in NOx increases at the higher engine load.
10% decrease
2% decrease
Fisher, B. C., Marchese, A. J., Volckens, J., Lee, T. and Collett, J. (2010). Measurement of Gaseous and Particulate Emissions from Algae-Based Fatty Acid Methyl Esters. SAE Int. J. Fuels Lubr. 3, pp.

## Slide 36
PM Mass Emissions
PM mass emissions decreased substantially for all of the B100 methyl esters in comparison to ULSD at the high engine loading condition.
At the lower engine loading condition, Algae 1 B100 had increased PM emissions in comparison to ULSD.

## Slide 37
All of the B100 methyl esters resulted in a decrease in the mean mobility diameter.
The PM size distribution from several of the methyl esters including Algae 1 B100 exhibited a nucleation mode peak centered between 10 and 20 nm.
PM Size Distribution
B100 Fuels
50% Load
75% Load

## Slide 38: Elemental and Organic Carbon
The PM from all of the methyl esters contained substantially higher quantities of volatile organic carbon in comparison to ULSD, particularly at the lower engine loading condition.
Algae 1 B100 had the highest ratio of OC:EC of all the fuels tested at both engine loading conditions.
50% Load
75% Load

## Slide 39
Review Algal Biofuels Conversion Technologies
Overview
  Motivation for Algal Biofuels
  The Algal Biofuel Value Chain Revisited
  Algal Methyl Ester Biodiesel Properties
  Algal Synthetic Paraffinic Diesel/Jet Fuel Properties
  Algal Hydrothermal Liquefaction Oil Properties
  Conclusions

## Slide 40
Review Algal Biofuels Conversion Technologies
Overview
  Motivation for Algal Biofuels
  The Algal Biofuel Value Chain Revisited
  Algal Methyl Ester Biodiesel Properties
  Algal Synthetic Paraffinic Diesel/Jet Fuel Properties
  Algal Hydrothermal Liquefaction Oil Properties
  Conclusions

## Slide 41: Conversion of Algal Lipids into Liquid Fuels Algal Renewable Diesel/Jet Fuel

## Slide 42
Renewable Jet Fuel from Algal Oil is Approved for Use
ASTM D7566-11
  In July 2011, ASTM passed specifications that allow use of renewable jet fuels produced from vegetable, algal oil and animal fat feedstocks.
  ASTM D7566-11 allows a 50 per cent blending of fuels derived from hydroprocessed esters and fatty acids (HEFA) with conventional petroleum-based jet fuel.
  ASTM D7655-11 is currently only valid for HEFA processes.

## Slide 43: Conversion of Algal Lipids into Liquid Fuels Algal Renewable Diesel/Jet Fuel

## Slide 44: Conversion of Algal Lipids into Liquid Fuels Algal Renewable Diesel/Jet Fuel

## Slide 45: Conversion of Algal Lipids into Liquid Fuels Algal Renewable Diesel/Jet Fuel

## Slide 46: Conversion of Algal Lipids into Liquid Fuels Algal Renewable Diesel/Jet Fuel

## Slide 47: Conversion of Algal Lipids into Liquid Fuels Algal Renewable Diesel/Jet Fuel

## Slide 48
Review Algal Biofuels Conversion Technologies
Overview
  Motivation for Algal Biofuels
  The Algal Biofuel Value Chain Revisited
  Algal Methyl Ester Biodiesel Properties
  Algal Synthetic Paraffinic Diesel/Jet Fuel Properties
  Algal Hydrothermal Liquefaction Oil Properties
  Conclusions

## Slide 49
Review Algal Biofuels Conversion Technologies
Overview
  Motivation for Algal Biofuels
  The Algal Biofuel Value Chain Revisited
  Algal Methyl Ester Biodiesel Properties
  Algal Synthetic Paraffinic Diesel/Jet Fuel Properties
  Algal Hydrothermal Liquefaction Oil Properties
  Conclusions

## Slide 50: Conversion of Whole Algal Biomass into Fuels Hydrothermal Liquefaction (HTL)
Hydrothermal liquefaction uses water at sufficient temperature and pressure to convert a wet biomass feedstock directly into a liquid bio-crude oil.
By processing the feedstock wet, the need for drying is eliminated.
Process temperatures are lower compared to dry pyrolysis.
  Current process conditions for the continuous flow system at PNNL are just below the supercritical point of water (350⁰C, 3000 psi).
Elliott, D. and Oyler, J. (2012). Hydrothermal processing: Efficient production of high-quality fuels from algae. 2nd International Conference on Algal Biomass, Biofuels and Bioproducts, San Diego, CA, June 2012.
Bench Scale
Reactor at PNNL
Simplified Process Diagram

## Slide 51: Conversion of Whole Algal Biomass into Fuels Hydrothermal Liquefaction (HTL)
Hydrothermal liquefaction uses water at sufficient temperature and pressure to convert a wet biomass feedstock directly into a liquid bio-crude oil.
By processing the feedstock wet, the need for drying is eliminated.
Process temperatures are lower compared to dry pyrolysis.
  Current process conditions for the continuous flow system at PNNL are just below the supercritical point of water (350⁰C, 3000 psi).
Feedstock: Wet Nannochloropsis salina Paste
HTL Bio-Oil
Hydrotreated HTL Bio-Oil
Fractionated cuts: naphtha, diesel, bottoms

## Slide 52: Conversion of Whole Algal Biomass into Fuels Hydrothermal Liquefaction
PNNL Process: Continuous Flow HTL of Whole Algal Biomass

## Slide 53: Conversion of Whole Algal Biomass into Fuels Hydrothermal Liquefaction
PNNL Results: HTL of Whole Algal Biomass
Parameter | Data
Lipid content of whole algae | 33%
Bio-oil from HTL as % algae mass | 58%
Bio-oil from HTL as % algae AFDW | 64%
% of algae carbon in HTL oil | 69%
Nannochloropsis salina from Solix BioSystems
Sample was frozen after harvest—no processing or lipid extraction
Wet algae paste, approximately 21% solids.
Elliott, D. and Oyler, J. (2012). Hydrothermal processing: Efficient production of high-quality fuels from algae. 2nd International Conference on Algal Biomass, Biofuels and Bioproducts, San Diego, CA, June 2012.

## Slide 54: Conversion of Whole Algal Biomass into Fuels Hydrothermal Liquefaction
Schaub, et al. (2012). Lipid Feedstocks, Produced Ester Fuel and Hydrothermal Liquefaction Products of Nannochloropsis salina: Detailed Compositional Analysis by Ultrahigh Resolution FT-ICR Mass Spectrometry 2nd International Conference on Algal Biomass, Biofuels and Bioproducts, San Diego, CA, June 2012.

## Slide 55: Conversion of Whole Algal Biomass into Fuels Upgrading of Hydrothermal Liquefaction Bio-Oil
Conversion and upgrading of HTL bio-oils
  Hydrotreating for O, S and N removal
  Hydrocracking/isomerization to finished fuel
  Produces renewable (non-oxygenated) fuel

## Slide 56: Conversion of Whole Algal Biomass into Fuels Upgrading of Hydrothermal Liquefaction Bio-Oil
HTL Bio-Oil
Hydrotreated HTL Bio-Oil
Fractionated cuts: naphtha, diesel, bottoms

## Slide 57
Review Algal Biofuels Conversion Technologies
Overview
  Motivation for Algal Biofuels
  The Algal Biofuel Value Chain Revisited
  Algal Methyl Ester Biodiesel Properties
  Algal Synthetic Paraffinic Diesel/Jet Fuel Properties
  Algal Hydrothermal Liquefaction Oil Properties
  Conclusions

## Slide 58
Review Algal Biofuels Conversion Technologies
Overview
  Motivation for Algal Biofuels
  The Algal Biofuel Value Chain Revisited
  Algal Methyl Ester Biodiesel Properties
  Algal Synthetic Paraffinic Diesel/Jet Fuel Properties
  Algal Hydrothermal Liquefaction Oil Properties
  Conclusions

## Slide 59: Conclusions
Phototropic microalgae is a potentially scalable liquid biofuel
The “ambitious” U.S. biofuels goal is 36 billion gal/year by 2022.
300 billion gal/year will be needed in future generations.
  Conventional Lipid to Liquid Fuel Conversion Technologies
  Fractionation necessary (and perhaps desirable) for some algal methyl esters.
  Hydrotreated renewable alkanes (diesel, jet) are ready for scale up.
  Preprocessing of crude lipid extracts must be considered. Not all extracts are alike and they differ from vegetable oil.
  Direct Conversion of Whole Algal Biomass to Liquid Fuels
  Hydrothermal liquefaction looks promising. Can be considered a high-yield, feedstock agnostic, wet extraction process.
  Upgrading to drop-in fuels for jet or diesel via hydrotreating is possible.
  New certification process would be necessary for HTL jet fuel.

## Slide 60
Questions?