## Slide 1: River Measurement Techniques
Haider Addab Neil A. Hadimoeljono Ramsey Pickard
Cive 717 – River Mechanics
Spring 2015

## Slide 2: Outline
Objectives
Basic Principles
Accuracy
River Measurement Techniques
  Stage Measurements
  Velocity Measurements
  Discharge Measurement Structures
  Sediment Sampling Techniques

## Slide 3: Objectives
Understand some basic principles of river measurement techniques
Present several river measurement techniques for:
  Discharge / flow measurements
  Sediment measurements
Provide some information about the accuracy of river measurement devices

## Slide 4: Basic Principles Critical Flow
Downstream wave or pressure disturbance cannot travel to upstream
Froude number = 1
For a given discharge, it produces a minimum specific energy
D
D
Equivalent section in terms of hydraulic mean depth (D))

## Slide 5: Accuracy
Errors and uncertainties classification:
  Spurious errors, caused by accident and resulting in false data like misreading and intermittent mechanical malfunction. Can be minimize by maintenance, inspection and training.
  Systematic errors, caused by deviations from standard devices dimensions. Can be corrected by maintenance, adjusting to accurate dimensional measurements or replacement of the device.
  Random errors, for example, when estimating required between the smallest division of head measurement device and water surface waves. Can be decreases with repeating readings
  Total errors, result of systematic and random errors.

## Slide 6: Stage Measurements
Stage gages are vertical boards or rods precisely graduated with reference to a datum
Point gages consist of mechanical or electromagnetic devices to locate and measure the water surface elevation. Lidars can be used for field measurements.

## Slide 7: Velocity Measurement Rotating Current Meters
Horizontal-axis meters act as a propellers in a moving fluid. Common meters included the Ott and the Neyrpic current meters.
Rotating current meters are useful to determine time-averaged flow velocity.
Rotating current meters are based on the proportionality between the angular velocity of the rotating device and the flow velocity. By counting the number of revolution of the rotor in a measured tie interval, point velocity is determined.

## Slide 8
The depth-averaged velocity is normally obtained from a time-averaged velocity profile. The following approximate methods for turbulent flows can be used to determine the depth-averaged flow velocity from point velocity measurements:
  The one point method (at 60% of the total depth measured down from the water surface) uses the observed time-averaged velocity at 0.6 h as the mean velocity in the vertical. This method gives reliable results in uniform cross-sections.
  The two point method (at 20% and 80% of the total depth measured down from the water surface) averages the two velocity measurements.
  The three point method (at 20%, 60%, and 80% of the total depth measured down from the water surface) averages the one point and two point methods.

## Slide 9
Velocity Measurement Acoustic (ultrasound)
Acoustic velocity meters measure velocity by determining the travel time of sound pulses transmitted and back scattered from small articles moving with the fluid.
Acoustic Doppler Current Profilers (ADCP) provide instantaneous velocity profiles in a cone from the point of measurement.
The measurement is not as good very near or vary far from the instrument.

## Slide 10: Velocity Measurements
Electromagnetic flow meters are based on Faraday’s induction law stating that voltage is induced by the motion of a conductor perpendicular to a magnetic field.
Hot film and hot wire anemometers are electrically heated sensors being cooled by advection. The heat loss being a function for the flow velocity, this laboratory instrument is calibrated to measure fluctuating velocities with high spatial resolution and high frequency response.

## Slide 11: Cross Section Geometry
Cross-section geometry can be measured using a steel tape and rod and level.
The steel tape is used to measure the width of the channel.
The rod and level measured relative elevation.
Measurements are taken at a tenth of the stream length.

## Slide 12: Bank Stability
Immediate results save the owner and engineer time and money, particularly with failed slopes
Measures the drained shear strength of soils in place
A new development allows for residual effective shear strength measurements
Used for designing earth slopes, retaining walls and determining the bearing capacity of foundations

## Slide 13: River Measurement Strucuture Discharge Measurement
Type of discharge measurement structure:
  Weirs
    Sharp-crested weir
    Broad-crested weir
  Flume
    Long-throated flume
    Short-throated flume
    Special flume
Source: http://www.usbr.gov/pmts/hydraulics_lab/pubs/wmm/chap07_13.html

## Slide 14: River Measurement Strucuture Discharge Measurement
Main consideration to select a measuring structure:
  Accuracy requirements
  Cost (construction, operation and maintenance)
  Range of flow rates
  Head loss
  Ability to pass sediment

## Slide 15: River Measurement Strucuture Discharge Measurement
Site selection consideration:
  To prevent excessive curvature of streamlines, channel reach upstream should be relatively straight and uniform for a distance about 10 times average channel width
  To ensure relatively smooth surface, Froude number upstream should be less than 0.5 for a distance of 30 yards
  To prevent water surface fluctuation, the minimum distance from any upstream structure should be 20 times water surface width at maximum flow
  Avoid placing structure in location where the soil characteristics are unsuitable.

## Slide 16: Weir Discharge measurement
Sharp crested weir (when H1/l ≥ 15).
There are 2 condition:
  Free flow
  Submerge flow, when the submergence (S) is bigger than critical factor (Sc). Thus Qsw should be multiplied by submergence factor (fs)

## Slide 17: Weir Discharge measurement
Broad crested weir (when 0.70 ≥ H1/l ≥ 0.07).
There are 2 condition:
  Free flow
  Submerge flow, when the submergence (S) is bigger than critical factor (Sc). Thus Qbw should be multiplied by submergence factor (fs)

## Slide 18: Weir Discharge measurement
Free flow is preferred than submerge flow,
  Submerge flow tends to be more inaccurate than free flow, because submergence factor (fs) only predict the value of submerge flow.
  Submerge flow needs 2 field data (y2 and y1)
Broad crested is preferred than sharp crested,
  Because broad crested weir has a bigger critical submergence (Sc), so the probability of submerge flow in broad crested weir is less than in sharp crested weir

## Slide 19: Flume Discharge Measurement
Structure that cause a critical flow in a channel by either a width contraction or a combination of width and relatively small bottom contraction
Classes:
  Long-Throated Flumes
  Short-Throated Flumes
  Special Flumes

## Slide 20: Flume Discharge Measurement
Long-Throated Flumes, have a throat that long enough to cause nearly parallel flow line

## Slide 21: Flume Discharge Measurement
Short-Throated Flume (Parshall Flume), which control flow in a region that produces curvilinear flow.

## Slide 22: Flume Discharge Measurement
Special Flumes
  Cutthroat Flume, resembles Parshall Flume with the throat “cut out”.

## Slide 23: Auxiliary Equipment Discharge measurement structures
Head measurement station
Staff gage
Recording gage
Stilling well
Staff gage
Continuous water gage recorder

## Slide 24: Sampling Techniques for Sediment
Sampling the water-sediment mixture for
  Determine the mean suspended sediment concentration,
  Particle size distribution,
  Specific gravity,
  Temperature of the water sediment mixture,
  Other physical and chemical properties of the transported solids.
Sampling frequency
  Generally dictated by the study approach and level of funding
Types of sediment samplers:
  Bed Sediment Samplers.
  Suspended Sediment Samplers.
  Bed load samplers.

## Slide 25: Bed sediment sampling
Shallow Samplers:
  Drag bucket samplers.
  Scoop samplers.
  Grab bucket or clamshell samplers.
  Vertical pipe or core samplers.
  Piston core samplers
  Rotating bucket samplers.

## Slide 26: Bed sediment sampling
Benefits:
  Particle size distribution
  Density of sediment particles
  Discharge of bed material by analytical method

## Slide 27: Bed sediment sampling
Drag bucket Sampler :
  Consist of weighted bucket with a cutting edge.
  Lowered to the bed & dragged in the upstream direction by a tow line operated from boat.
They are not taking a sample from a single spot.
Mix the material scooped from the different depths penetrated.

## Slide 28: Bed sediment sampling
Scoop Samplers:
  One end is closed.
  Other end beveled to provide cutting edge.
  Used up to 6 m depth.
  Could collect samples from top 60 mm of the bed.
  A hinged cover plate may be placed over the cutting edge of the sampler.

## Slide 29: Bed sediment sampling
Grab bucket sampler:
  Work very good in sandy stream.
  Do not close properly if the sample contains gravels or clay.
  Consist of cupped jaws which are closed at the bed to trap the sample.
  Could collect samples from top 125 mm of the bed.
  Special control is required to ensure the representative of the bed material.

## Slide 30: Bed sediment sampling
Vertical pipe or core:
  Consist of tube forced into the stream bed.
  Good quality sample.
  less disruptive than dredge or grab samplers.
  Easy to use in fine grained bed but its hard to use in sand bed.
  Inexpensive samples &simple to maintain.

## Slide 31: Bed sediment sampling
Piston core sampler: (US BMH-53)
  Consist of (9x2)in pipe with cutting edge and suction piston .
  The piston is retracted as the cutting cylinder is forced into the streambed.
  Used in shallow streams.

## Slide 32: Bed sediment sampling
Deep sampler:
  Rotating bucket sampler: (US BM 60)
    Designed for sand-bed streams.
    The sampler can be suspended from a handline or sounding reel.
    The bucket, in closing, penetrates the streambed and completely encloses a sample of material.
    30 IB weight.

## Slide 33: Bed sediment sampling
Deep sampler:
  Rotating bucket sampler: (US BM 54)
    Designed to be suspended from a cable and to scoop up a sample of the bed sediment that is 3 in width and 2 in max depth.
    When the sampler contacts the stream bed with the bucket completely retracted , the tension in the suspension cable is released & heavy coil spring quickly rotates the bucket through 180 degree to scoop up the sample.

## Slide 34: Bed sediment sampling
Rotary-bucket bed material sampler: (US RBMH-80)
  hand-operated sampler that has a semi-cylindrical bucket for collecting the bed material samples.
  It is constructed from lightweight aluminum and uses a BM-54 sample bucket.
  Operation is simple: the lever on the handle opens and closes the bucket.

## Slide 35: 2. Suspended Sediment Sampler
Instantaneous suspended sediment samplers
  Trap a volume of suspension flowing through a cylindrical tube by simultaneously closing off both ends.
  Bucket sampling from the free surface also considered as instantaneous sampler.

## Slide 36: 2. Suspended Sediment Sampler
Point Integrating Samplers:
  The point-integrating sampler remains at a fixed point in the stream and samples continuously during the time it takes for the bottle to fill.
  The dried sample measures the time average d sediment concentration
  During the sampling period , the valve is opened and the air escapes the sampler at a nozzle intake velocity nearly equal to the local stream velocity.
  The body of the sampler contains air which is compressed by the inflowing liquid .

## Slide 37: 2. Suspended Sediment Samplers

## Slide 38: 2. Suspended Sediment Samplers
Depth Integrating Samplers:
  Gives a single sample combined from small sub-samples taken from different points.
  Lowered from the water surface to the streambed and returned at a constant rate of travel.
  Ascending and descending speeds need not be the same, but the rate of travel must be constant in each direction.
  Air in the container is compressed so that the pressure balances the hydrostatic pressure at the air exhaust
  The inflow velocity is approximately equal to the stream velocity.

## Slide 39: 2. Suspended Sediment Samplers
Depth Integrating Samplers

## Slide 40: 3. Bed load Measurements
Bed load traps
  Sampling initiation of gravel motion and coarse bed load transport rates in wadable gravel and cobble bed mountain streams.
  The trap is temporarily fastened onto ground plates anchored into the stream bottom.
  This capability for representative sampling provides valuable bedload data-sets suitable for performing initial motion computations.

## Slide 41: 3. Bed load Measurements
Tracer Techniques:
  Coarse bed material.
  Painting, staining or radio tracking coarse particles from the bed.
  Positions of particles indicates the distance traveled during the flood and reflect sediment transport .

## Slide 42: 3. Bed load Measurements
Haley-Smith sampler:
  Suited to coarse sand to fine gravel bed streams.
  Long period of sampling could clog the sample bag.
  Very coarse material(ds>80 mm) will not enter the sampler & very fine material(ds<0.5 mm) will be washed.

## Slide 43: References
Geol 642. Fluvial Geomorphology – Field Trip Manual.
Julien P. Y., (2010). Erosion and Sedimentation. Cambridge University Press, Cambridge, UK.
http://www.rickly.com/index.htm
U.S. Bureau of Reclamation, (2001). Water Measurement Manual. U.S. Government Printing Office, Washington, DC.
Voltman W. F., (1989). Discharge Measurement Structures 3rd ed. International Institute for Land Reclamation and Improvement, Wageningen, The Netherlands.