## Slide 1
Nuclear Energy
Foundations & State of the World for Systems Engineers
Vincent Paglioni, Ph.D.
Assistant Professor of Systems Engineering
Vincent.Paglioni@colostate.edu

## Slide 2: About me
Education
B.S., Nuclear & Radiological Engineering
  Georgia Institute of Technology (2017)
M.S., Reliability Engineering
  University of Maryland (2022)
Ph.D., Reliability Engineering
  University of Maryland (2023)
Experience
Nuclear Test Engineer
  Portsmouth Naval Shipyard (2017 – 2019)
Assistant Professor
  Colorado State University (2023 - )

## Slide 3: Nuclear Development in the U.S.
Under construction in western US:
  MSR-1 @ Abilene Christian University
  TerraPower Natrium (Kemmerer, WY)
  Pele & Molten Chloride demos (Idaho)
  Aalo-X (Idaho)
Planned for western US:
  4 X-energy Xe-100 @ Dow Seadrift (TX)
  4 Westinghouse AP-1000 @ DJTGP (TX)
  1 Oklo Aurora (Idaho)
  1 Westinghouse eVinci demo (Idaho)
  3-4 SMRs @ TAMU Rellis Campus (TX)
  1 BWXT Rx (Green River, WY)
4x nuclear would add ~300,000 jobs across trades and professions
SERIOUS money in nuclear right now
A quick analysis (thanks, ChatGPT) estimates $100B* in quantifiable PPAs and other support mechanisms
80-90% is related to AI in some way
NPV $20B (high risk)

## Slide 4: Overview
Nuclear Fundamentals: Radiation & Fission
Reactor designs
Future of Nuclear Power
Health, Environmental, and Cultural issues
Resources

## Slide 5: Radiation and Fission

## Slide 6: Radiation: The Basics
Radiation is energy (or particles) emitted by excited atoms
  Nonionizing radiation: EM waves
    E.g., radio waves, microwaves
  Ionizing radiation is our concern
Types of ionizing radiation:
  Alpha (; nucleus)
    Heavy, charged, low range
  Beta (; electrons or positrons)
    Small, charged, medium range
  Gamma (; photons)
    Massless, chargeless, long range
  Neutron ()

## Slide 7: Nuclear Fission: What is it?
Fission splits atoms with neutrons to produce energy
  Fissile nuclides (U-235) undergo fission with low-energy neutrons
A neutron is captured & splits U-235 into 2-3 pieces
  These fragments break off and release more neutrons
A chain reaction can be formed if enough U-235 is compiled together
  A reactor is critical if the chain reaction is self-sustained
Each fission reaction destroys U-235 and produces fission products
  These can be radioactive & long-lived, and must be stored for long-term…

## Slide 8: Nuclear Reactors

## Slide 9: Nuclear Power Plant Basics
Make Heat
Reactors use nuclear fission (splitting atoms)
Some coolant absorbs the heat for use
2. Use Heat
Spin a turbine to produce electricity, add heat to thermal storage system, etc.
Images: https://3d.energyencyclopedia.com/npp-pwr
3. Expel Waste Heat
No thermal power plant uses all heat
Waste heat sent to environment or synergistic industry

## Slide 10
Images: https://3d.energyencyclopedia.com/npp-pwr

## Slide 11: Dr. P’s Quick Keys: Nuclear Reactors
1. Fission Chain Reaction
2. Neutron Energy
4. Control
Fuel captures neutron, forms compound nucleus that stretches and deforms
Fragments break off & release more neutrons
  Fragments become fission products
3. Cooling
Fission neutrons released with high energies (MeV)
U-235 needs lower neutron energies for effective fission
Fast reactors need no moderator, but near-term designs (Westinghouse AP-1000, NuScale) use water moderator
Cooling System | Use (gal/MWh) | Water Removed (gal/MWh)
Fossil; once-through | 20,000 – 50,000 | 300
Nuclear; once-through | 25,000 – 60,000 | 400
Fossil; cooling tower | 500 – 600 | 380 – 440
Nuclear; cooling tower | 800 – 1100 | 520 – 660
Fossil; pond cooling | 270 – 500 | 270 – 500
Nuclear; pond cooling | 500 – 1100 | 400 – 700
Water & Sustainability (Volume 3): U.S. Water Consumption for Power Production—The Next Half Century, EPRI, Palo Alto, CA: 2002. 1006786 |  | 
Cooling needed to control reactor temperature, develop useful work
Multiple working fluids available for primary coolant
  H2O, D2O, CO2, Helium, molten salts, liquid metals, etc.
Generally use water for secondary system to drive turbine
PASSIVE/INHERENT CONTROL
Inherent: negative MTC, FTC limit thermal runaway
Passive: freeze plugs, natural circulation, dump tanks, etc. place reactor in safe condition without operator action or powered device
ACTIVE CONTROL
Control rods manipulable to change power level
Pressurizer controls (PWR) for pressure/temperature adjustments
Emergency core cooling systems
https://www.nuclear-power.com/nuclear-power/fission/
https://en.wikipedia.org/wiki/Fission_barrier#cite_note-1
https://www.researchgate.net/publication/375232437_Physics_of_Nuclear_Explosives_Chapters_1_and_2
https://3d.energyencyclopedia.com/npp-pwr/

## Slide 12
Early, “proof of concept” reactors – some also produced fuel for weapons. Last Gen I shut down in 2015 (Wylfa-2).
First reactors designed specifically for power. Larger units with active safety features. 85% of nuclear power produced by Gen II.
Gen III/III+ improved safety, efficiency, operational life.
Gen III+ includes AP-1000.
Envisioned as next-generation. Designs selected in 2000 include GFR, LFR, MSR, SFR, SCWR
Notes: GFR: Gas-cooled fast reactor
LFR: Lead-cooled fast reactor
MSR: Molten salt reactor
SFR: Sodium-cooled fast reactor (terrapower)
SCWR: Supercritical water cooled

## Slide 13: Small Modular Design Paradigm
Smaller size & power, modular build
  New siting opportunities
  Lower up-front cost = broader applications
Gen III+ or Gen IV:
  NuScale’s Power Modules ~ Gen III+ iPWRs
  TerraPower’s Gen IV SFR
Multiple benefits:
  Passive safety, potentially “walk-away safe”
  Limited emergency planning zone (EPZ)
  Support for micro- and off-grid applications
  Cogeneration
Top: https://www.world-nuclear-news.org/articles/nuscale-integrated-energy-system-desalination-clean-hydrogen
Bottom: https://www.terrapower.com/natrium/

## Slide 14: Small
SMR
Up to ~400 MWe
“Site boundary” EPZ
  Smaller source term lowers doses
  New siting allowances
Lower on-site construction
LLWR
Up to 1000 MWe (3500 MWth)
EPZ up to 16km from reactor
  NPP emergency management
Significant on-site construction
  Systems too large to pre-fabricate

## Slide 15: Modular
LLWR
Higher construction costs with site-specific design variation
Long construction time with significant onsite work
Minimal opportunities for cross-fleet sharing of components
SMR
Lower construction costs with factory construction
Reduce construction time with minimal onsite work
Interoperability across fleet
  Operators & components can move between sites
Source: Motive Power National Public Utility Council

## Slide 16: NuScale: Gen III+ iPWR
Only NRC-approved SMR in the U.S.
250 MWt (77 MWe) per module
  “integrated”  Primary loop components inside RPV
  Multi-unit sites; 1 control room
CONOPS and reactor behaviors well understood
Critical novelty: multi-unit control room
Capacity Factor | > 95%
Fuel & Cycle | < 4.95% UO2, 18-21 month
RPV & Core | 76’ x 15’ (2m core height)
Steam Temp | < 500 F @ Turbine
Capacity Factor | > 95%
Fuel & Cycle | < 4.95% UO2, 18-21 month
RPV & Core | 76’ x 15’ (2m core height)
Steam Temp | 
NuScale can produce >900F steam for industrial applications
Figure: 3D Model - Small Modular Reactor - Energy Encyclopedia
September 2025: NuScale, ENTRA1 and Tennessee Valley Authority announce 6 GW deployment of SMRs throughout TVA service territory.
That is SIX 12-unit power plants!

## Slide 17: TerraPower: Gen IV SFR
Reactor Power | 840 MWt (345 MWe)
Fuel & Cycle | 5 – 20% (HALEU) U metal
2 Temp | > 900F
Reactor Power | 840 MWt (345 MWe)
Fuel & Cycle | 5 – 20% (HALEU) U metal
Only SMR under construction in the U.S.
Gen IV Na (metal) fast reactor with molten salt energy storage
  Grid decoupling
Novel CONOPS and Rx behaviors
  Passive safety changes operator role
Fast Rx  SNF transmutation

## Slide 18: Nuclear Fuel Cycle: Front-end Overview
Recovery
  Traditional deep-shaft or open-pit mining
  In situ recovery (ISR) methods
Milling
  Concentrating ore to uranium oxides
    Most common is U3O8 (yellowcake)
Conversion
  U3O8 is chemically converted to UF6
  UF6 is kept natural or enriched (~5%)
Fuel Fabrication
  UF6 is converted to UO2 powder, pressed into pellets, sintered to form ceramics
  UO2 pellets loaded into Zircaloy tubes

## Slide 19: Nuclear Fuel Cycle: Back-end Overview
Interim Storage
  Spent Fuel Pools at individual reactor sites
  Dry Cask Storage at ISFSI
    Independent Spent Fuel Storage Installations
    Applications pending for Consolidated Interim Storage Facilities (CISFs) in NM, TX
Reprocessing
  Actinides and transuranic elements removed
    Useful radionuclides isolated for medical, industrial uses
    Pu, U refashioned into Mixed Oxide (MOX) fuel
Disposal
  Theoretically, high-level waste is permanently disposed of to minimize environmental impact

## Slide 20: SNF Storage
Spent nuclear fuel (SNF) spends 5 years in pool so “hottest” isotopes decay
  Pools maintain water 20 ft above SNF
Pools and dry casks can store SNF for 60 years beyond operating license
  Casks licensed for 40 years, 40 yr extension
Interim storage facilities pose almost no threat to human or environmental health. Pools and dry casks are heavily monitored and rigorously tested.
There is currently no long-term storage solution in the U.S.
1982: Nuclear Waste Policy Act (NWPA) charges DOE with long geologic storage of SNF
  Federal govt to take ownership of SNF by 1998
1986: DOE selects three candidate sites
  Yucca Mountain, Deaf Smith (TX), Hanford (WA)
1987: NWPA amended: Yucca mountain only
  Effectively halted in 2000s

## Slide 21: Human, Environmental, and Cultural Safety

## Slide 22: What everyone really wants to know…
Colorado average background dose (incl. radon): 5-7 mSv/yr
  National average ~ 2-3 mSv/yr
  ~50% of CO homes over EPA radon guidelines
Why is Colorado so high?
  3rd largest U reserves in U.S.
  High altitude (cosmic radiation)
  “Downwind”, mining, and Rocky Flats provide no significant dose to Coloradans
Avg. CO background
1/10 lowest level linked to cancer
Lowest level linked to increased cancer
Acute problems start here
(100x CO bkgd)
Maximum permissible dose to public from NPP is 0.25 mSv/yr
Average much lower (0.0001)

## Slide 23: Nuclear & Water
Cooling System | Use (gal/MWh) | Water Removed (gal/MWh)
Fossil; once-through | 20,000 – 50,000 | 300
Nuclear; once-through | 25,000 – 60,000 | 400
Fossil; cooling tower | 500 – 600 | 380 – 440
Nuclear; cooling tower | 800 – 1100 | 520 – 660
Fossil; pond cooling | 270 – 500 | 270 – 500
Nuclear; pond cooling | 500 – 1100 | 400 – 700
Water & Sustainability (Volume 3): U.S. Water Consumption for Power Production—The Next Half Century, EPRI, Palo Alto, CA: 2002. 1006786 |  | 
Isotope | PWR Median Release [Ci] (2021) | BWR Median Release [Ci] (2021)
H-3 (Tritium) | 538 | 5.02
Co-58 | 1.47E-03 | 0
Co-60 | 9.91E-04 | 7.51E-04
Cs-137 | 1.84E-05 | 8.94E-07
Maldonado, D. (2024). Radioactive Effluents from Nuclear Power Plants: Annual Report 2021. U.S. Nuclear Regulatory Commission Office of Nuclear Reactor Regulation, Division of Risk Assessment. Rockville, MD USA. |  | 
NPPs release a small amount of radioactive material during normal operations.
These releases are governed by EPA and NRC.
The maximum dose permitted to non-workers from operations is 0.25 mSv/yr (1/200 limit for nuclear workers).

## Slide 24: Community & Environmental Impact
The ONLY ETHICAL PATH is to work with communities
Communities understand their own needs and deserve some self-determination in local administration matters
Particularly for communities previously affected by nuclear enterprise activities (e.g., Native Nations & Peoples, Downwind communities), building back trust is imperative
  Trust is built through honest, open, frank communication and acknowledging the cultural, communal and personal impacts of nuclear energy
Notes: Three Mile Island: people forced to evacuate their homes in PA
Chernobyl: 32 direct deaths of plant workers and first responders, thousands of cancers, 1000 square miles of territory forcibly evacuated
Bikini Atoll: In all we detonated 23 weapons on the atoll. Residents were “voluntarily” relocated in 1946 on the understanding that they would be able to return soon. To this day, Bikini Islanders have not been allowed back
Nevada Test Site: Built on 600+ square miles of land taken from Western Shoshone peoples. 1,021 nuclear tests from 1951 to 1992. The ~900 underground test pockmarked the land and added some 300 MegaCuries of radioactivity into the land
Rulison Test Site (Colorado): Part of Project Plowshare, three underground detonations were conducted off I-70 in Colorado. The site remains unusable for habitation.

## Slide 25: Future of Nuclear Energy: Novel Benefits & Risks

## Slide 26: Novel Reactors, Novel Benefits (1)
SMRs
Monetary Benefits
Industrial Growth
Civic Growth
Lower “overnight” capital costs open new deployment opportunities
  Smaller utilities & co-ops
  Private non-utility funding
  Behind-the-meter feasibility
Produce lucrative products to supplement NPP income
  1000 MWe reactor could produce 150,000 tons of H2 /yr (DOE)
  > $42M additional revenue (EIA)
https://www.fuelcellenergy.com/blog/low-cost-hydrogen-production-from-nuclear-energy

## Slide 27: Novel Reactors, Novel Benefits (2)
SMRs
Monetary Benefits
Industrial Growth
Civic Growth
Nuclear power growing other industries
Artificial Intelligence & Computing:
  Google: 500MW PPA (Kairos)
  Amazon: $500M (X-Energy)
  Microsoft: PPA (TMI)
Chemical Industry:
  DOW x X-energy (Seadrift, TX)
Electricity & heat-driven cogeneration:
Hydrogen production
Waste water treatment
District heating/cooling
Cogeneration produces secondary jobs beyond NPP operation

## Slide 28: Novel Reactors, Novel Benefits (3)
SMRs
Monetary Benefits
Industrial Growth
Civic Growth
Nuclear power plants employ more people at higher wages than comparable fossil fuel or renewable power plants
Community population and tax base growth
Lower GHG emissions improves quality of life
Notes: Job satisfaction is priceless, and coal-to-nuclear transition maintains the ethos of energy jobs for communities where that is actually important

## Slide 29: Novel Reactors, Novel Risks (1)
Technical Risks
Mission Risks
Financial Risks
Multi-unit control
Passive safety & automation
New siting = new ETs
Cogeneration = new ETs
FOAK Construction
FOAK Fuel Cycle
Technical risks arise from novel concept of operations (CONOPS)
Multi-unit Control room:
  Operators will have to control multiple quasi-independent reactors
  Reactors sharing resources & systems induces potential common-cause failures (CCFs)
Passive Safety:
  Poorly-defined approaches to risk and reliability analysis of passive systems
  No operator action for envisioned events, but potential for skill atrophy
Automation:
  Software reliability and risk analysis methods poorly-defined
  Changing role of operator = significant changes to human reliability analysis (HRA)

## Slide 30: Novel Reactors, Novel Risks (2)
Technical Risks
Mission Risks
Financial Risks
Multi-unit control
Passive safety & automation
New siting = new ETs
Cogeneration = new ETs
FOAK Construction
FOAK Fuel Cycle
Mission risks from novel contexts of operation
Site-boundary EPZ:
  Opens siting closer to population centers
  May introduce new initiating events for PRA
    E.g., complications from municipal events
  Level 1 and 3 PRA could be affected
Cogeneration:
  Co-located industrial processes introduce new initiating events and branch points, e.g.:
    IE: H2 leak = new initiating event
    BP: Rx SCRAM and H2 facility effects
Off-grid/remote operation:
  Remote operations = novel threat vectors
  Complication in case of emergency

## Slide 31: Novel Reactors, Novel Risks (3)
Technical Risks
Mission Risks
Financial Risks
Multi-unit control
Passive safety & automation
New siting = new ETs
Cogeneration = new ETs
FOAK Construction
FOAK Fuel Cycle
Financial risks arise from novelty in general
Construction:
  FOAK construction costs almost always high
  FOAK SMR costs could jeopardize industry
  “Vaporware” potential
Fuel Cycle:
  HALEU, TRISO fuel cycle facilities, regulations
    Centrus has HALEU production license
    TRISO production? HALEU transport?
  SNF disposition always a consideration
FOAK-NOAK Transition
  FOAK-NOAK transition holds logically and evidenced by Gen II, Vogtle 3-4 construction
  HOWEVER – requires “fast followers” to leverage institutional knowledge, workforce

## Slide 32: DOE Reactor Development Programs
Adv. Reactor Demonstration Program (ARDP)
Announced in 2020
Support 10 reactor designs in various stages of development
DOE support, but licensed under NRC regulations
Reactor Pilot Program (RPP)
Announced in 2025
Support 10 reactor designs; 3 critical by July 4, 2026
Authorized under DOE rules, not NRC regulations
  Subject to recent DOE categorical exemption changes

## Slide 33: Resources
Nuclear Energy Institute (NEI - https://nei.org):
  Education resources, events/training, information, public policy
Idaho National Lab Gateway for Accelerated Innovation in Nuclear (GAIN - https://gain.inl.gov/):
  Community engagement, industry support, information
American Nuclear Society (ANS - https://www.ans.org/):
  Technical expertise, community engagement, outreach support
  Colorado local section under development
CO Nuclear Alliance (https://www.coloradonuclearalliance.org/):
  Policy advocacy, community engagement
Nuclear Works (https://nuclearworks.org/):
  General information, career advice (all levels), networking, job listings

## Slide 34: Thank you!
Vinnie Paglioni: Vincent.paglioni@colostate.edu