## Slide 1
River Confluences
Farid Karimpour
Josh Smalley

## Slide 2: Definition/Objective
  The meeting of two or more rivers is called a river confluence.
  Usually a river is the main stream and others are the tributaries.
  Objective is to study the river confluences effects and characteristics

## Slide 3: Physical Processes
Downstream of a river confluence, if the sediment concentration and grain size remain constant, can be expected to be:
  Significantly wider
  Deeper
  Experiences more shear stress
  Slightly faster
  Slight decrease in slope

## Slide 4: Physical Relationships

## Slide 5: Confluence Formation
Confluences primarily form as the drainage network originally forms, but can also form through:
  River capture
  Human induced changes
Teay River capture by the Ohio

## Slide 6: Confluence Migration
River Confluences tend to be static through time
Slackwater zones form downstream of wide bars
  This induces rapid deposition and maintains a streamline confluence
From Julien, 2002

## Slide 7: Mississippi confluence with the Red
Atchafalaya provides shorter distance
Naturally would have captured Mississippi
Flow diversion from Mississippi is managed
Human managed confluence

## Slide 8
Amazon River

## Slide 9: Amazon Confluences
Confluence of the Marañón and the Ucayali
15,000 sub-branches join the Amazon

## Slide 10
Flow diagram at a 90 river confluence

## Slide 11: Mixing Zones
Mixing zones occur downstream of river confluences
Distance till mixing can be approximated by:
Where:

## Slide 12
Mixing length depends primarily on width, depth, velocity, and shear velocity
An increase in shear velocity or depth will decrease mixing length
An increase in width or velocity will increase mixing length

## Slide 13: Numerical Simulations

## Slide 14
Iso-concentration curves(left figure), Dispersion (right figure)

## Slide 15
Distribution of the vertical vorticity, in the instantaneous flow in a horizontal surface situated at (left) 0.1 D and (right) 0.5 D below the free surface.

## Slide 16
Left) Distribution of the mean streamwise velocity, us (m/s), in section A1.
Right) Distribution of the streamwise‐oriented vorticity, in the mean flow at sections A1, A, and C (As shown in slide 15)

## Slide 17: Natural Confluences
Glacier and spring fed streams in Ecuador

## Slide 18
Shallow mixing layers developing at the river confluences

## Slide 19
Photographs of Lake Powell at the confluence with the Dirty Devil River (entering from left).

## Slide 20: References
Constantinescu, G., Miyawaki, S., Rhoads, B., Sukhodolov, A., Kirkil, G., “Structure of turbulent flow at a river confluence with momentum and velocity ratios close to 1: Insight provided by an eddy‐resolving numerical simulation”, Water Resources Research, vol. 47, w05507, doi:10.1029/2010wr010018, 2011
Julien, P. Y., “Erosion and Sedimentation”, Cambridge Press, 2010
Julien, P. Y., “River Mechanics”, Cambridge Press, 2002
Petrescu, V., Sumbasacu, O., “Comparison between numerical simulation and measurements of the pollutant dispersion in a river. case study”, U.P.B. Sci. Bull., Series D, Vol. 72, Iss. 3, 2010
Roca, M., Martín-Vide, J.P., Moreta, P.J.M., ” Modelling a torrential event in a river confluence”, Journal of Hydrology 364 (2009) 207–215