## Slide 1: Headcut Prevention
CIVE 717: Assignment #4
John Quebbeman, Andrew Steininger, Rachel Williams
April 12, 2012

## Slide 2: This presentation is presented in three sections:
Headcut Equations- John Quebbeman
Physical Process and Model- Andrew Steininger
Design and Prevention Methods- Rachel Williams

## Slide 3: Headcut Equations
April 12, 2012

## Slide 4: Headcut Equations
Hydraulic Equations
Sediment Transport Equations
Numerical Models (SITES)
Empirical Quantification
Photo Source: WES Stream Investigation and Streambank Stabilization Handbook, US Army Corps of Engineers, October, 1997

## Slide 5: Hydraulics
Critical Depth – Occurs over top of headcut
Normal Depth – Commonly assumed for downstream channel below headcut
  Used for Shear Stress Calculations
Shear Stress – Bed Shear used for determining transport capacity
hc=critical depth
hn=normal depth
V=velocity
n=Manning Roughness
g=gravitational constant
S=Friction Slope
h=depth
γ=Specific Weight

## Slide 6: Sediment Transport
Downstream Erosion & Channel Deepening
  Sufficient Capacity to Transport Bed Sediment
  Supply<Capacity, Simplified Estimate
Transport Capacity Estimates (Julien, 2002)
  Sediment Discharge by Volume
Approaches may be used to find unstable channel conditions

## Slide 7: Numerical Model
Software Available for Calculating Headcut
USDA – NRCS developed SITES Model
Mainly developed for Headcut Calculation of Earthen Embankments (may be applied for instream applications)
Headcut Phases in SITES Model
  Phase 1 – Erosion of Vegetal Surface Layer
  Phase 2 – Deepening of erosion, Start of Headcut
  Phase 3 – Headcut Migration Upstream

## Slide 8: SITES Model - Phase II
USDA Ch. 51, Part 628 Dams, Earth Spillway Erosion Model
Surface Detachment
Partial Vegetal Cover
Erosion Deepening
Effective Shear w/ Partial Vegetal Cover
Erosion Rate
Shear Stress
Erodibility Coefficient

## Slide 9: SITES Model – Phase III
Phase III Erosion
Depth >Critical Depth
Upstream Advance & Deepening
Checks for Normal Depth Shear vs. Drop Shear
Normal Depth Shear
Drop Depth Shear
Check for Maximum Shear:

## Slide 10: SITES Headcut Advancement
Phase III Erosion
Headcut advances upstream if threshold exceeded
<A0 is No Movement
Based on Shields Approach for Incipient Motion

## Slide 11: SITES Hydraulic Jump
Stress Estimate Uses Simplified Horizontal Assumptions
Normal Depth in Downstream Channel
Energy Slope & Sequent Depth used to determine Shear Stresses

## Slide 12: SITES Erodibility of Multiple Layers
Erodibility Index Kh
Steps through time considering eroded layer i
Composite
Erodibility Index
Erodibility Index
Layer ‘i’
Thickness
Layer ‘i'
Total Thickness

## Slide 13: Empirical Headcut Advancement Rate
Studied in SW US
Migration Upstream
F(x) of Precipitation times Drainage Area
May vary with different regions
Rieke-Zapp, D., Nichols, M. Headcut Retreat in a Semiarid Watershed in the Southwestern United States Since 1935, Catena, Vol 87, Issue 1, October, 2011.

## Slide 14: The Physical Process Model of Headcutting
Watson etal 2007 Stream Rehabilitation

## Slide 15: Headcutting Causes:
Natural:
  Base level drop
    Earthquakes or tectonic processes
  Ground water sapping
    Topographically caused ground water concentration
    piping
  Change in sediment regime
    fire induced runoff
    Draught or Flooding
Human Induced:
  Change in sediment regime
    Increased sediment input to a reach from agriculture or timber harvest
    Decreased sediment input to a reach due to stream bank armoring
  Change in flow regime
    Increased runoff from urban areas
  Change in base level
    Change in output elevation/water level (i.e. reservoirs)

## Slide 16: The overall controls on headcutting conditions
http://weltanschuuang.blogspot.com/2009_11_01_archive.html
Streams naturally tend toward a state of “dynamic equilibrium”. This state is typified by the following characteristics:
Longitudinally uniform energy dissipation (limited local areas of large energy head change)
Sediment continuity (the sediment input to a stream equals the output)
A sediment capacity supply ratio (CSR) of 1
Constant Slope (no substantial aggradation or degradation)
Lane’s Balance represents the balance of driving variables in a stream system

## Slide 17
http://myweb.cwpost.liu.edu/vdivener/notes/streams_basic.htm
Natural Stability and Headcut Prevention
Headcuts can be prevented by maintaining the natural watershed condition with regard to flow, sediment and slope.

## Slide 18: The Local Physical Mechanism for a Headcut
Increased flow velocity over a headcut continues erosion at the head cut depth in the upstream direction manifesting the head cut feature head ward.
Diagram of water level and energy distribution at a headcut
http://www.agu.org/journals/wr/wr0509/2004WR003752/
Example of a numerical model simulation of the headcut flow

## Slide 19: Physical Modeling of the Headcutting Process
http://www.colorado.edu/geography/geomorph/rosenberry/

## Slide 20: Common Drainage Patterns Caused by Head ward Erosion
Trellis – form in repeating layers of stronger and weaker substrate material
Dendritic Pattern– form in homogenous landforms where substrate material has no control over flow direction
Rectangular Pattern – form in bedrock which is jointed at 90 degree angles

## Slide 21: Ground water Seepage Headcutting
Dunne, 1980. (a) A stream valley erodes into a headland, causing a slight deflection and concentration of ground-water discharge; (b) the concentrated ground-water discharge results in sapping which erodes a small cut into the side of the headland, which further concentrates ground-water discharge and sapping; (c) the newly formed headcut erodes further, and sidecuts may develop and erode in the direction of sediment jointing or faulting.
http://www.colorado.edu/geography/geomorph/rosenberry/

## Slide 22: Base level lowering Headcut
http://www.colorado.edu/geography/geomorph/rosenberry/
Headcutting is commonly a mechanism for channel adjustment to a large scale change in slope.

## Slide 23: Channel Widening
Headcutting can cause downstream incision and bank failure causing channel widening
Watson etal 2007 Stream Rehabilitation

## Slide 24: Headcutting is out of this world!
http://www.colorado.edu/geography/geomorph/rosenberry/
Short, deep, stream-like channels on Mars may be the result of ground-water sapping (Gulick, 2001).
Features on Mars generated substantial interest in studies of ground-water sapping during the 1980s and early 1990s.

## Slide 25: Design and Prevention Methods
This section discusses considerations for the prevention of forming headcuts and the control of existing headcuts.
Headcuts can be described with a channel evolution model. Ideally they should be controlled at Phase 1 before they begin or before Phase 3 when bank failure occurs.

## Slide 26: Headcut Prevention
Preventing head cuts can be done by avoiding practices that cause change in hydraulic or sediment continuity including:
Straightening channels (ΔSo)
Gravel mining (ΔD50)
Land Use change (ΔQ & D50)
inc. Farming, road construction, grazing, mining, urbanization
Bledsoe, Stream Rehabilitation, 2011

## Slide 27: Mitigating Land Use Change
Land Use change cannot always be avoided but the impacts on flow regime change can be mitigated with stormwater management by:
encouraging groundwater infiltration
retaining storm runoff and slowly releasing it
natural plant cover buffers around streams
http://www.apexnc.org/services/public-works/
http://landscapeandurbanism.blogspot.com

## Slide 28: Grade Control Structures
Existing headcuts can be controlled with grade control structures placed either above or below the headcut. The structure causes the aggradation of sediment above it and decreases the bed slope from S1 to S2 as in the figure.
Height of structure = (S1-S2)*L
The equilibrium bed slope (S2) is found by analyzing the stable slopes for a sediment transport rate. Methods such as SIAM and Copeland’s can be utilized.

## Slide 29: Types of Grade Control Structures
In choosing the type of structure you must consider frequency and number of structures and other criteria such as cost, material availability, environmental impacts, and risk.
Some examples include:
Large, single drop structures
Drop box culvert
Smaller drops (Sheet pile, rock, gabien)
Rock Ramps (Newbury riffles)
Rosgen structures
Chester Watson, USACE

## Slide 30: Large single-drop structure
Chester Watson, USACE
Grade control for large head cuts can be achieved with single large structures.
Advantages:
Only one structure
Lower risk of failure
No scour hole with concrete slab
Disadvantages:
Expensive
No fish passage
Flood management
Appearance

## Slide 31: Drop Box Culvert
A drop box culvert controls a hydraulic jump at a bridge structure. It is similar to the previous example
Chester Watson, USACE
Advantages:
Only one structure
Limits risk to bridge infrastructure
No scour hole with DS concrete slab
Disadvantages:
Expensive
No fish passage
Flood management
Appearance

## Slide 32: Smaller Weir Structures
Grade control for a head cut can also be achieved with smaller, cheaper structures. Depending on the scenario one or more weirs may be necessary. They can be constructed using various materials. Locally they are often large rocks.
Sheet Pile Weir: Useful when rock is not readily available, but can still prevent fish passage
Rock Gabiens: The gabiens function as a weir and are cheaper than large rock but are more succeptible to erosion failure
Chester Watson, USACE

## Slide 33
Smaller Weir Structures
Rock ramps dissipate energy over a longer area with large rocks
Advantages: cheaper, can allow fish passage, natural looking
Disadvantages: requires rock, rocks may more in large floods
Newbury, Newbury Hydraulics
Chester Watson, USACE
Newbury Riffles (below) are another example of rock ramps that allow fish passage and grade control.

## Slide 34
Rosgen, Wildland Hydrology
Smaller Weir Structures
Rosgen has designed several structures that are used as grade control including cross-vanes, J-hooks, and W-weirs. They are constructed of large rocks, and often can allow fish passage.