## Slide 1: Grade Control Structures
Chris Shrimpton and Jonathan McIntosh
CIVE 717 River Mechanics
Spring 2012

## Slide 2: Objectives
General objectives are to stabilize channel banks and bed by:
  Reducing the slope of the channel
  Reducing flow velocity
  Dissipating energy from the flow
  Reducing bank height
Best for smaller rivers and streams

## Slide 3: Channelization
A
B
Lane’s relationship: QS+ α Qs+Ds
Plan View
Profile View

## Slide 4
h > hc
h < hc
Reduce bank height
Reduce bed slope

## Slide 5: Grade Control Placement
Upstream of headcut
Downstream of headcut
Headcut
Headcut
Aggradation

## Slide 6: Types of Grade Control
Log Crib Drop Structures
Sloping Sills
  Sloping Riprap
  Grouted Boulder
  Baffle Shoot
Weirs
  Sheet Pile
  Concrete
  Rock

## Slide 7: Log Crib Drop Structures
Best for small streams and gullies
Low cost for materials and simple construction
Most effective for small drops
Can be implemented in series with other log crib structures

## Slide 8: Sloping Sills
Popular, versatile drop structures
Can facilitate various drop heights
Frequently constructed with grouted riprap or boulders, as observed on the CIVE 717 field trip
Two categories for design: above and below ground

## Slide 9: Primary Design Considerations
Above Ground
  Up and downstream hydraulics
  Height of drop
  Aesthetics, public safety, etc.
Below Ground
  Foundation
  Seepage control
  Soil and groundwater conditions

## Slide 10: Primary Design Considerations
Special attention where design intersects channel bed/soil
Sufficient excavation and soil compaction to prevent undercutting by the flow
Utilize filters to prevent erosion of underlying material
Armor channel on downstream end to prevent scour

## Slide 11: Types of Sloping Sills
Sloping Riprap Drop:

## Slide 12: Types of Sloping Sills
Grouted Sloping Boulder Drop:

## Slide 13: Types of Sloping Sills
Baffle Shoot Drop Structure:

## Slide 14: Comparison of Sloping Sill Types
Study by Urban Drainage and Flood Control District in Denver area
Grouted sloping boulder drops more effective than traditional sloping riprap structures.

## Slide 15: Weirs - Sheet pile
Advantages
  Simple to design
  Inexpensive
  Good for wide rivers
Disadvantages
  Bad for deep rivers
  Poor aesthetic quality

## Slide 16: Weirs - Concrete
Advantages
  Durable
  Can be used for flow measurement
Disadvantages
  Expensive
  Cost prohibitive for large rivers
  Prevent fish passage

## Slide 17: Weirs - Rock
Advantages
  “Natural” appearance
  Inexpensive to construct
  Allow fish passage
Disadvantages
  Only for small streams
  Easily mobilized
  Large boulders may not be available

## Slide 18: Prevent Structural Failure
Size appropriately
Dissipate energy
  Riprap upstream and downstream
  Concrete slab
Tie into banks
  Prevent flow from flanking
Use filters

## Slide 19: Conclusions
Objectives:
  Reduce channel slope
  Stabilize banks
  Energy dissipation
Constraints:
  Consider size/depth of river
  Cost
  Available materials
Design:
  Tie into banks
  Maintain conveyance

## Slide 20: Questions?

## Slide 21: References
Introduction to Grade Control Structures by Chester Watson
River Mechanics by Pierre Y. Julien, Ph.D.
http://www.alluvium.com
http://www.nrcs.usda.gov
http://www.udfcd.org